## Slide 1: Materials for Civil and Construction Engineers
CHAPTER 1
Materials Engineering Concepts
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 2: 1.7 Material Variability
All materials have variability
  Some materials are more uniform than others
    Steel vs. concrete vs. wood
Error vs. blunder
Three sources of variance:
  Material
  Sampling
  Testing
Use good sampling and testing techniques to minimize those variabilities
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 3
Precision: measure many times and get same result
Bias: tendency to deviate in one direction from true value
Accuracy: close to true value; absence of bias
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 4: Sampling
Proper sampling must ensure that a random and representative sample is taken from the population (e.g., stockpile, lot, etc.)
  Random: have an equal chance of being selected
  Representative: perfect average of the entire stockpile
Sample size:
  depends on materials variability & tolerance level of results
  more variability dictates a larger sample
Rigorous statistical evaluations required for special applications:
  high quality asphalt and portland cement concrete
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 5: Problem 1.47
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 6
Describes many populations that occur in nature, including material properties
Area under the curve between any two values represents the probability of occurrence
Normal Distribution
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 7: Material Property Data Analysis
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.
Arithmetic average or Mean
Standard Deviation (s or s)

## Slide 8
Decrease inspection frequency
Early detection of troubles
Provide a record of quality
Basis of acceptance
Control Charts
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.

## Slide 9: Experimental Error
Caused by 3 factors:
Procedural errors
  are often undiscovered
Machine errors (bias)
  if known and constant can be easily corrected
Human errors
  minimize by repetition, double-checking, etc.
    Always do more than one test
Mamlouk/Zaniewski, Materials for Civil and Construction Engineers, Fourth Edition. Copyright © 2017 Pearson Education, Inc.